Experiment No 2

Objective: - Study and performance test on a four-stroke single cylinder diesel engine at 			constant speed.

ENGINE SPECIFICATIONS:

Engine Type : Single cylinder Four stroke Diesel engine(Kirloskar), Bore : 0.0875m, Stroke : 0.11m Capacity : 661.5 cc, Power : 6 H.P. at 1500 rpm, Torque : 2.96 kg.m at 1500 rpm and Compression Ratio :17.5:1

Measurement of:-

- Fuel consumption.

- Inclined manometer readings for air flow.

- RPM, power output etc.

- Study of various components of diesel engine.

Prerequisites: -

- Explain the air-fuel ratio ?

- What are the methods of available for improving the performance of an engine?

- Distinguish between power and specific output?

- What is the importance of specific fuel consumption?

Experimental Procedure/what you should aim at: -

- Draw a neat sketch of the test rig.

- Measurement of load and manometer readings.

- Measure the fuel consumption and draw curves BTE,BSFC Vs load.

- Measurement of frictional power by Willan's line method.

What next (Things you can ponder over):-

- Why did I do this whole experiment? (What is the technical applicability in real world?)

- What are the different methods for measurement of frictional power?

- Define Willan's lines methods?

- Why is a large flywheel flywheel  required in a single cylinder diesel engine and not in multi cylinder engine

- Define the friction power.

Submission of Report:

- A single report per group.

- All are equally responsible for the preparation of the report.

- Should answer the question on your report.

- Each Report will be evaluated for 10 points.

References:-(Books to consult)

- IC Engines by V Ganesan.