Experiment No 6

Objective: - Study of Operation and Performance analysis of turbochargers.

Prerequisites: -

- Why Turbochargers?

- A brief knowledge of turbochargers.

- An idea about compressor maps.

- A well introduced idea about Boost pressure and other terminologies used in turbocharger studies.

- …

- …

- …

Minute details about the practical Setup :-( or the theoretical brief background):-

A turbocharger is a positive feedback unit, in which as exhaust flow increases, the turbine of the turbocharger increases, which increases the pressure or boost supplied to the intake system. As engine rpms increase, turbo boost increases to a point where the wastegate regulates it.

Today's vehicles are being equipped more and more with turbochargers. To understand what they do, we'll explain how they work. A turbocharger is made up basically of 3 sections: a center body consisting of the shaft housing, an intake housing and an exhaust housing. The center housing is a shaft with the turbine fins attached on each side; the bearings and seals of the shaft are in the center housing. Now that you have found it, you can take the cover off.

Working of Turbochargers:

The exhaust of the engine flows through the exhaust housing and turns the turbine on the exhaust side, which in turn turns the intake turbine that pressurizes the air going into the intake. There is a wastegate on the exhaust side that regulates how much of the exhaust pressure is applied to the turbo and how much bypasses it. Without the wastegate, the pressure could build to a point of destroying the engine. The wastegate is the turbocharger's "failsafe", for lack of a better term.

The air to the intake is usually cooled by an intercooler, which uses the engine cooling system to reduce the high temperature of the air before it goes into the intake system. The cooler the air into the cylinders, the denser the fuel/air mixture can be. So for optimum efficiency, the air going into the cylinders needs to be as cool as it can be.

Normally most problems occur with turbochargers when foreign debris gets into the turbine blades and binds the turbines or when the oil drain tube becomes clogged with hardened oil that has gone from the extreme heat of the turbo to the cooler oil drain tube. When the oil drain tube becomes clogged, the oil builds up in the center housing, having place to go, it pushes out the shaft seals and often creates an extremely smoky engine. With regular oil changes and servicing, turbochargers can be pretty reliable.

A turbocharger is an exhaust-driven air compressor. It becomes an air compressor by utilizing expanded exhaust gases from the engine. The exhaust gas pressure and the heat energy extracted from the gas causes the turbine wheel to rotate, thus driving the compressor wheel through a common shaft. Exhaust temperature and pressure drop as they pass through the turbine housing and into the atmosphere. The rotating compressor wheel draws air in and the blades accelerate and expel the air into the compressor housing. Once into the compressor housing, the air is compressed and flows toward the intake manifold, pressurizing the intake in a measurable form we call boost pressure.

Figure : I.C. Engine with Turbocharger

#### Figure 2:  Elements of Turbochanrger

#### CASE STUDY :

#### We have two different experiments:-

#### We have a Toyota MR2 turbocharger whose turbine is run by compressed air rather than exhaust from an engine. This is used for studying the effect at various flow rate of fluid entering the turbocharger, where as we have an Indica V-2 turbocharger which is attached to a Maruti Zen engine. Here the turbocharger is run by the exhaust of the engine.

The Compressor:

Here's a comparison chart of turbo compressor wheel and turbine wheel. Not necessarily sorted by size and power.

| Turbo | Compressor | Turbine |
| --- | --- | --- |
|  | Wheel Trim map avail | Inducer Diameter (in./mm) | Exducer Diameter (in./mm) | Housing | CFM | Wheel Trim | Exducer Diameter (in.) | Inducer Diameter (in.) | Flange style, Housing size |
| Stock TB02/22 | T2 | 1.57"/40mm | 2.02"/51mm | TB22 | 304 max | T22 69 | 1.53"/38.9mm | 1.85"/47mm | T25 |
| Garrett T25 | T25 60 | 1.66"/42mm | 2.14"/54.4mm | TB25 | 405 max | T25 62 | 1.64"/41.7mm | 2.09"/53mm | T25 |
| Garrett T28 | T3 60 | 1.83"/46.5mm | 2.37"/60mm | TB03 | 448 max | T25 62 | 1.64"/41.7mm | 2.09"/53mm | T25 |
| JWT 500 |  | 1.53"/38.9mm? | 2.06"/52mm? | TB22 |  | T25 | 1.59"/40.4mm | 1.83"/45.7mm | T25 |
| JWT 530BB GT25R/GT2554R | GT25R 60 | 1.65"/42mm | 2.14"/54.3mm | GT25R |  | GT25 62 | 1.64"/41.7mm | 2.09"/53mm | T25 .64 A/R |
| JWT 600 | T3? 60? | 1.83"/46.5mm | 2.37"/60mm | TB25 |  |  | 1.86"/47.2mm | 2.09"/53mm? | T25 |
| JWT 650 | T3 63 | 1.89"/48mm | 2.37"/60mm | T3 | 506 max | T3 | 1.86"/47.2mm | 2.09"/53mm | T25 |
| JWT 700 BB GT28RS/GT2860R | GT28RS 62 | 1.86"/47.2mm | 2.37"/60mm | GT28RS | 535 max | GT28 76 | 1.85"/46.9mm | 2.09"/53.9mm | T25 .86 A/R |
| GT2871R | GT2871R 48 | 1.94"/49.2mm? | 2.79"/71mm? | GT28RS | 599 max | GT28 76 | 1.85"/46.9mm | 2.09"/53.9mm | T25 .86 A/R |
| PE 1420 | ? 57 | 1.79"/45.5mm | 2.37"/60mm | ? | 494 max | P20 84 | 1.73"/44 | 1.89"/48mm | ? |
| PE 1820 | ? 55 | 2.07"/52.5mm | 2.76"/70mm | ? | 635 max | P20 84 | 1.74"/44.7 | 2.047"/52mm | ? |
| Greddy TD04H-15C | 15C 55 | 1.65"/42mm | 2.187"/55.5mm | TD04 |  | TD04H | 1.74"/44.7 | 2.047"/52mm | TD04H 3bolt |
| Greddy TD05-16G | 16G 60 | 1.83"/46.5mm | 2.236/57mm | TD05 | 520 @2PR | TD05H | 1.93"/49mm | 2.20"/56mm | TD05H 6,7,8cm2 3bolt |
| Greddy TD05-18G | 18G 50 | 1.99"/50.5mm | 2.68/68mm | a* | ? @2PR | TD05H | 1.93"/49mm | 2.20"/56mm | TD05H 6,7,8cm2 3 bolt |
| b* Greddy TD06-20G | 20G 60 | 2.07"/52.6mm | 2.68"/68mm | TD06 | 685 max | TD06S | 2.17"/55.1mm | 2.56"/65mm | TD06S 8,10cm2 3 bolt |
| HKS GT2530 | GT28RS 63 | 1.90"/47.7mm | 2.37"/60mm | T3 63 | 477 max | GT25 | 1.85"/47mm | 2.12"/54mm | T25 .64 A/R T3 |
| HKS GT2540 | T04E 46 | 2.1"/51.7mm | 3"/76mm | To4E 46 | 564 @2PR | GT25 | 1.85"/47mm | 2.12"/54mm | .64 A/R |
| b*HKS GT2835 d* | GT35 52 | 2.01"/51.2 | 2.79"/71mm | GT35 | 608 max | GT28 | 2.01"/51.8mm | 2.23"/56.5mm | T25 .61, .73 |
| c*HKS GT3037 d* | GT37 52 | 2.17"/55mm | 3.00"/76mm | GT37 | 709 max | GT30 | 2.16"/55mm | 2.36"/60mm | T25 |
| Garrett GT3071R | GT37 56 | 2.08"/53mm | 3.00"/71mm | GT37 | 694 max | GT30 | 2"/50.8mm | 2.22"/56.5mm | T25 flange .86 A/R |
| Garrett GT3076R | GT30R 56 | 2.24"/57mm | 3.00"76.2mm | GT37 | 752 max | GT30 | 2.16"/55mm | 2.36"/60mm | T3flange .82, 1.06 A/R |
| *Turbonetics T3/To4B | To4B S | 1.90"/48.2mm | 2.75"/70mm | To4B S | 520 @2PR | T3 | 2.05"/52.1mm? | 2.35"/59.7mm? | T3 |
| *Turbonetics T3/To4E | To4E 60 | 2.29"/58.2mm | 2.95"/75mm | To4E 60 | 650 @2PR | T3 | 2.05"/52.1mm? | 2.35"/59.7mm? | T3 |

Standard Compressor Flow Maps

Experimental Procedure/what you should aim at: -

- Collect all the details of the engine mentioned above.

- Calculate the amount of air required for different boost pressures and engine speeds.

- Study the compressor chart given above.

- Calculate the operating points of the compressor for various engine speeds.

- Calculate the increase in power output of the engine.

What next (Things you can ponder over):-

  - Why did I do this whole experiment?

  - What are the different manufacturing companies involved in making turbochargers?

  - Can I find the historical lineage of how turbochargers of the day came into being?

  - What are the different large and small turbocharger applications?

  - Does the use of turbochargers have environmental consequences? What are they?

Submission of Report:

  - A single report per group.

  - All are equally responsible for the preparation of the report.

  - Should answer the question on your report.

  - Each Report will be evaluated for 10 points.

References:- (Material to consult.)

    - www.tpub.com

    - www.autozine.com

    - www.turbobygarret.com

    - www.enginelogics.com (for compressor maps)

    - Maximum Boost by Corky bell.

    - …

    - ..