## Slide 1: Extended Surfaces for Better Thermal Management of Chip on Board
Shape Evolution of Heat Exchanging Surfaces…
P M V Subbarao
Professor
Mechanical Engineering Department

## Slide 2: Forced Convection Cooling of Chips Using Air

## Slide 3: Analytical Convective Heat Transfer
1701 Newton’s law of cooling.
1822: Fourier’s Conduction Equation.
In the 1807 memoir, Fourier successfully developed a formula to use Newton’s Law as
This was incorporated by Fourier into his epoch-making convective boundary condition.
In 1915 Nusselt cut the Gordian knot.
Boundary layer conduction was used as boundary condition to define Nu or h.
Blending of Convection & Conduction in to GDE was a need for design high energy dissipating systems.
1945 - GARDNER-MURRAY Ideas.

## Slide 4: Clues from Nature: Blending of Convection or Radiation in Conduction Equation
Body to gain or loose heat
Extended surface
Continuous Convection or Radiation heat transfer to/from fin surface
Conduction heat transfer to /from body.
Conduction through the fin is strengthened or weakened by continuous convection or radiation from/to fin surface.

## Slide 5: Mathematical Ideas are More Natural
Reptiles, mammals and birds like high steady body temperatures.
They have sophisticated ways to manage flows of heat between their bodies and the environment.
Body shape enters the physics of body cooling.
It also helps to explain the odd appendages like crests and sails that decorated extinct reptiles like Stegosaurus or mammal-like reptiles like Dimetrodon.
Theoretical Biologists did Calculations to show these structures could act as very effective heat exchange fins.
These fins are allowing animals with crests to heat their bodies up to high temperatures much faster than animals without them.

## Slide 6: Natural Geometries for Convection Cooling
An optimum body size is essential for the ability to regulate body temperature by blood-borne heat exchange.
For animals in air, this optimum size is a little over 5 kg.
For animals living in water, the optimum size is much larger, on the order of 100 kg or so.
This may explain why large reptiles today are largely aquatic and terrestrial reptiles are smaller.

## Slide 7: Amalgamation of Conduction and Convection/Radiation

## Slide 8: Basic Geometric Features of Fins
profile
PROFILE AREA
cross-section
CROSS-SECTION AREA

## Slide 9: Innovative Fin Designs

## Slide 10: Single Fins :Shapes
Longitudinal or strip
Radial
Pins

## Slide 11
Anatomy of A STRIP FIN
thickness
x
Dx
Flow Direction

## Slide 12: GARDNER-MURRAY ANALYSIS : ASSUMPTIONS
Steady state one dimensional conduction Model.
No Heat sources or sinks within the fin .
Thermal conductivity constant and uniform in all directions.
Heat transfer coefficient constant and uniform over fin faces.
Surrounding temperature constant and uniform.
Base temperature constant and uniform over fin base.
Fin width much smaller than fin height.
No bond resistance between fin base and prime surface.
Heat flow off fin proportional to temperature excess.

## Slide 13: Slender Fins
thickness
Dx

## Slide 14: Steady One-dimensional Conduction through Fins
qx
qx+dx
qconv or qradiation
Conservation of Energy:
OR

## Slide 15: Transverse Heat Transfer in A Fin
OR
thickness
Dx

## Slide 16: Governing Differential Equation for Conjugate Heat Transfer
qx
qx+dx
conv
Energy Conservation Equation per unit length of fin :
Taking limit Dx tends to zero and using the definition of derivative:

## Slide 17: Governing Differential Equation for Conjugate Heat Transfer
qx
qx+dx
conv
Substitute Fourier’s Law of Conduction:

## Slide 18
Types of Strip Fins with Reduced Weight
Straight fin of triangular profile rectangular C.S.
Straight fin of parabolic profile rectangular C.S.
L
x=0
b
x=b
x
qb
L
b
qb
x=b
x=0
x

## Slide 19
Fins with Cartesian Geometry Heat Transfer
Straight fin of triangular profile Circular C.S.
Straight fin of parabolic profile rectangular C.S.

## Slide 20
Fins with Cylindrical Geometry Heat Transfer
Circumferential fin of rectangular profile
Straight fin of triangular profile

## Slide 21
Strip Fin with constant cross section area:

## Slide 22: The Fin Factor
Fin factor for pin Fin:
Fin factor for strip Fin:

## Slide 23: GDE for Constant CS Area Fins
Define:
At the base of the fin:

## Slide 24: Conditions at the Tip of A Fin

## Slide 25
Conditions at the Tip of A Fin

## Slide 26: Linear Second order ODE with Constant Coefficients
This equation has two linearly independent solutions.
The general solution is the linear combination of those two independent solutions.
Each solution function qi(x) and its second derivative must be constant multiple of each other.
Therefore, the general solution function of the differential equation above is: