Experiment No 1

Objective: - Study and performance test on a four-stroke multi cylinder diesel engine at 			constant speed.

ENGINE SPECIFICATIONS:

Engine Type : Four cylinder Four stroke Diesel engine, Bore : 0.073m, Stroke : 0.0889m Capacity : 1489cc, Power : 36 H.P. at 4000 rpm, Torque : 8.5 kg.m at 2250 rpm and Compression Ratio :17.3:1

Measurement of:-

- Fuel consumption.

- Manometer readings for air flow.

- RPM, power output etc.

- Study of various components of diesel engine.

Prerequisites: -

- Explain the cold start?

- Type of dynamometer?

- Distinguish between power and specific output?

- What is the importance of specific fuel consumption?

Experimental Procedure/what you should aim at: -

- Draw a neat sketch of the test rig.

- Measurement of load and manometer readings.

- Measure the fuel consumption and draw curves BTE,BSFC Vs load.

- Measurement of frictional power byWillan's line method.

What next (Things you can ponder over):-

- Why did I do this whole experiment? (What is the technical applicability in real world?)

- What are the different methods for measurement of frictional power?

- Define Willan's lines methods?

- Define the friction power

Submission of Report:

- A single report per group.

- All are equally responsible for the preparation of the report.

- Should answer the question on your report.

- Each Report will be evaluated for 10 points.

References:-(Books to consult)

- IC Engines by V Ganesan