Experiment  No. 5

Performance and emission test of a dual fuel single cylinder four stroke compression ignition engine

Objectives:

- To understand the basic working principle of a dual fuel engine.

- To understand the benefits of a dual fuel engine when compared with the conventional combustion concept.

- To study the different parts and modifications done to a single cylinder diesel engine.

- To study the performance of a dual fuel engine.

- To study the emission characteristics of a dual fuel engine.

Experimental Procedure:

Experiment would be conducted for four different load conditions (no load, 1 kW, 2 kW and 3 kW) at a constant speed of 1300 rpm

- Draw a neat sketch of the test rig with detailed and clear labelling of  each instrument.

- Measurement of engine speed, load and fuel consumption.

- Measurement of manometer reading across the orifice to calculate air flow rates.

- Measurement of emissions.

- Measurement of temperatures.(inlet, exhaust, cylinder wall and lub oil)

Analysis of the results and report submission:

- Neat sketch of the experimental test rig .

- Performance study of a dual fuel engine.

- Brake power vs. load

- BSFC vs. load

- Brake power vs. SFC

- Brake thermal efficiency vs. load

- Emission behavior of the dual fuel engine

Plot a graph showing the variation of NOX, CO and HC emission with respect to load.

4	Calculate the mechanical efficiency of the dual fuel engine.

Observation table

| Sl. no | RPM | Fuel Cons. Mai(ml/min) | Load | Mano Reading (mm) | T₁ (°C) Intake | T₂ (°C) exhaust | T₃ (°C) Lub oil | T₄ (°C) Cyl. Wall temp. | CO (%) | CO₂ (%) | HC (ppm) | O₂ (%) | NOх (ppm ) | Smoke (opacity) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Curr. (Amp) | Vol. (v) |  |  |  |  |  |  |  |  |  |  |  |