Experiment  No. 6

Combustion parameter study of a single cylinder four stroke diesel engine

Objectives:

- To understand the different instrumentation used to study the combustion behavior of a single cylinder four stroke diesel engine.

- To understand the basic calculations to obtain different combustion parameters from in-cylinder pressure data.

Experimental Procedure:

Experiment would be conducted for three load conditions (no load, 2 kW and 4 kW) at a constant speed of 1350 rpm

- Draw a neat sketch with all major dimensions of the test rig.

- Measurement of rpm, load and fuel consumption.

- Measurement of manometer reading to calculate air flow rates.

- Measurement of temperatures.(inlet, exhaust, cylinder wall and lub oil)

- Measurement of in-cylinder pressure date from the acquisition system.

Analysis of the results and report submission:

Each report should include the following

1    Neat sketch of the experimental test rig.

2   Calculate the start of combustion and plot the same with respect to load.

3   Calculate the pressure rise rate(PRR) and heat release rate (HRR) from pressure data.

4   Plot the followings for three different load conditions:

- Crank angle vs pressure

- Crank angle vs HRR

- Crank angle vs PRR

5   Identify the crank angle at which peak pressure, peak PRR, peak HRR and SOC occurs. (for all 3 loads)

6   Make a plot of these four parameters (as in sl. No. 5) with their corresponding angle of occurrences. (for all three loads)

Observation table

| Sl. no | RPM | Fuel Cons. Mai(ml/min) | Load | Mano Reading (mm) | T₁ (°C) Intake | T₂ (°C) exhaust | T₃ (°C) Lub oil | T₄ (°C) Cyl. Wall temp. | CO (%) | CO₂ (%) | HC (ppm) | O₂ (%) | NOх (ppm ) | Smoke (opacity) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Curr. (Amp) | Vol. (v) |  |  |  |  |  |  |  |  |  |  |  |

Figure: Schematic diagram of experimental test rig.

| Type of engine | Kirlosker single Cylinder 4-Stroke Diesel engine |
| --- | --- |
| Bore(mm) | 102 |
| Stroke(mm) | 116 |
| Length of connecting rod(mm) | 230 |
| Compression ratio | 17.5:1 |
| Maximum power | 7.4kW@1500 rpm |

Table 1: detailed specifications of the engine

N.B. for calculations and analysis

The heat release rate is usually calculated by the following formula. [ Ref. J.B.Heywood]

Where=Rate of change of heat release w.r.t. crank angle,

Ө-crank angle in radian,   Rate of change of pressure w.r.t. crank angle,

=,    V=Volume of cylinder at any position of crank angle,

Instantaneous volume (V) is given as,

Where,= clearance volume, B=Bore, l=Length of connecting rod, a= crank radius, =S/2 , s= stroke length

Air flow rate calculation:

ṁa= ρair×cd×A√ (2g×Δhw× ρw /ρair)

ρair=P/(R×T)……………………………………………………….…............................(4)

Where,

ṁa=mass flow rate of air in kg/sec

ρair=density of air at room temperature in kg/m3

P=atmospheric pressure in N/m2

R= specific gas constant in J/kg.K

T=absolute temperature

cd=coefficient of discharge of orifice (take 0.62 )

A=area of orifice in m2 (take 20 mm as diameter)

Δhw= meno metric head in meter

ρw=density of liquid used in U-tube manometer in kg/m3

Fuel properties: Density of diesel is 0.832 kg/ltr, CV of diesel is 43 MJ/kg

Density of petrol is 0.720 kg/ltr, CV of petrol is 46 MJ/kg

Take the value of   as 1.32 for the calculation of HRR

# Text boxes

Fuel tank

2. Fuel Injector

1. Pressure Transducer

3. Thermo-couple

PPress

2

1

Air Drum

Charge Amplifier

Encoder

Engine

Gas Analyzer

Computer

Loading Panel

Dynamo

meter

PPress

NI Acquisition System